Experiment 2

; 8086 ALP to add n numbers and find average, average.asm
; In this program, we will initialise
; n numbers in memory location, add them and then find average
; Registers used: AX. CX, DX
; Ports used:

DATA SEGMENT
    N DW ? ;NUMBER OF NUMBERS
    SUM DW 0 ;SUM OF N NUMBERS
    AVG DB ? ;AVERAGE OF N NUMBERS
DATA ENDS

CODE SEGMENT
    ASSUME CS:CODE, DS:DATA

    START: MOV AX, @DATA ;LOAD DAYA SEGMENT
        MOV DS, AX ;INITIALISE DATA SEGMENT

        MOV AH, 01H ;INPUT
        INT 21H ;INPUT INTERRUPT
        AND AL, 0FH ;BCD FORM
        MOV AH, 0 ;SET AH TO 0
        MOV N, AX ;STORE VALUE OF N

        MOV CX, N ;COUNTER TILL N NUMBERS

    INPUT: MOV AH, 01H ;INPUT
        INT 21H ;INPUT INTERRUPT
        AND AL, 0FH ;BCD FORM
        MOV AH, 0 ;SET AH TO 0
        ADD SUM, AX ;KEEP ADDING INPUTS
        LOOP INPUT ;LOOP TILL N

        MOV AX, SUM ;MOVE SUM TO AX
        DIV N ;DIVIDE SUM BY N
        MOV AVG, AL ;MOV VALUE OF AVERAGE TO AVG

        MOV AH, 02H ;OUTPUT
        MOV DX, SUM ;STORE SUM IN DL FOR PRINTING
        ADD DL, 48 ;CONVERT TO ASCII
        INT 21H ;OUTPUT INTERRUPT

        MOV DL, AVG ;STORE AVG IN DL FOR PRINTING
        ADD DL, 48 ;CONVERT TO ASCII
        INT 21H ;OUTPUT INTERRUPT
CODE ENDS
END START