EXPERIMENT 3

;; 8086 ALP to find odd even number, OddEvenNumber.asm
; In this program, we will initialise
; 1 number in memory location, and check if it is odd or even
; Registers used: AX. CX
; Ports used:

DATA SEGMENT
    ITEMS_MSG DB 13, 10, "ENTER NUMBER OF ELEMENTS", '$'
    ITEMS DB ? ;NUMBER OF ELEMENTS
    NUM DB ? ;NUMBER OF NUMBERS
    EVEN DB 13, 10, "EVEN", '$' ;EVEN OUTPUT
    ODD DB 13, 10, "ODD", '$' ;ODD OUTPUT
DATA ENDS

CODE SEGMENT
    ASSUME CS:CODE, DS:DATA

    NEWLINE MACRO ;MACRO TO PRINT A NEW LINE
        MOV ah, 02h ;PRINT
        MOV dl, 10 ;NEW LINE ASCII
        INT 21h ;PRINT INTERRUPT
        MOV dl, 13 ;CARRIAGE RETURN ASCII
        INT 21h ;PRINT INTERRUPT
    ENDM

    START: MOV AX, @DATA ;LOAD DAYA SEGMENT
        MOV DS, AX ;INITIALISE DATA SEGMENT

        LEA DX, ITEMS_MSG;LOAD OFFSET TO PRINT
        MOV AH, 09H ;OUTPUT
        INT 21H ;OUTPUT INTERRUPT

        MOV AH, 01H ;INPUT
        INT 21H ;INPUT INTERRUPT
        AND AL, 0FH ;BCD FORM
        MOV ITEMS, AL ;STORE VALUE OF ITEMS
        MOV CX, ITEMS ;STORE ITEMS INTO CX, FOR LOOPING

        NEWLINE

    LOOP1: MOV AH, 01H ;INPUT
        INT 21H ;INPUT INTERRUPT
        AND AL, 0FH ;BCD FORM
        MOV NUM, AL ;STORE VALUE OF N
        AND AL, 01H ;GET LEAST SIGNIFICANT BIT

        CMP AL, 01 ;COMPARE LAST DIGIT TO 1
        JE EQUAL ;IF EQUAL
        JMP NEQUAL ;IF NOT EQUAL

    EQUAL: LEA DX, ODD ;IS ODD
        JMP PROGEND ;JUMP TO PROGEND

    NEQUAL: LEA DX, EVEN ;IS EVEN
        JMP PROGEND ;JUMP TO PROGEND

    PROGEND: MOV AH, 09H
        INT 21H
        NEWLINE
        LOOP LOOP1

CODE ENDS
END START